## Slide 1: Course Teacher: Md. Fahmidur Rahman Sakib Lecturer, Department of Computer Science & Engineering Metropolitan University
8086 Hardware Specifications
Course ID: CSE 237
Course Title: Microprocessor and Interfacing

## Slide 2: Lecture References:
Book:
  Microprocessors and Interfacing: Programming and Hardware, Author: Douglas V. Hall
  The 8086/8088 Family: Design, Programming, And Interfacing, Author: John Uffenbeck.

## Slide 3: 8086 Pin Specification
is a 40-pin DIPs; Dual in-line package
DIP refers to a rectangular housing with two parallel rows of electrical connection pins.
DIPs have a notch on one end to show its correct orientation.
The pins are then numbered as shown in the figure below.

## Slide 4: 8086 Pin Diagram
Recap
8086 is a 16-bit microprocessor.
Meaning it has 16 data lines/bus.
It has 20 address lines/bus.
Each memory location holds only 1 byte
Can address different memory locations
It could address up to 1MB of memory.
min mode
max mode

## Slide 5: 8086 Pin Specification
CLK
provides basic timing to control processor operation
frequencies of different versions are 5, 8 or10 MHz
asymmetric with a 33% duty cycle

## Slide 6: 8086 Pin Specification
lines are multiplexed bidirectional address/data bus.
During they carry 16-bit address.
In remaining clock cycles , 16-bit data.
carry lower order data byte
carry higher order data byte

## Slide 7: 8086 Pin Specification
lines are multiplexed address and status bus.
During they carry the highest order 4-bit address.
D, status signals.
, segment identifiers as in table below
S4 | S3 | Function
0 | 0 | Extra segment access
0 | 1 | Stack segment access
1 | 0 | Code segment access
1 | 1 | Data segment access

## Slide 8: 8086 Pin Specification
: Indicates if interrupt is enabled or disabled.
If =1 , then the IF = 1, so the interrupt is enabled.
If =0 , then the IF = 0, so the interrupt is disabled.
: Indicates if 8086 is the bus master or not
If = 0 , 8086 is the bus master
If = 1 , 8086 is not the bus master

## Slide 9: 8086 Pin Specification
Bus High Enable
is active low
To indicate the transfer of data over
Related to memory bank
Selects odd/high memory bank when is 0
: Reserved for further development

## Slide 10: 8086 Pin Specification
is active low
Indicates read operation when low
Processor reading from memory or I/O device
Is low during states of the read cycle

## Slide 11: 8086 Pin Specification
Is examined by the WAIT instruction.
If this pin is Low, execution continues.
Else the processor waits in an idle state.

## Slide 12: 8086 Pin Specification
READY
acknowledgement from a slow I/O device or memory
To indicate ready/completion of data transfer
When low, microprocessor enters wait state, .

## Slide 13: 8086 Pin Specification
RESET
To reset the system reset.
And terminates the current activity.
Must be active for at least four clock cycles

## Slide 14: 8086 Pin Specification
N
Non-maskable interrupt signal.
Causes a type-2 interrupt.
Initiates the interrupt at the end of the current instruction.
INTR
Interrupt request
Used to request a hardware interrupt.
Can be masked.

## Slide 15: 8086 Pin Specification
min mode
max mode
8086 works in two modes:
  Minimum Mode if high
  Maximum Mode if low
Functions of pins 24-31 depend on the mode
Minimum Mode - single processor
Maximum Mode - multi processor

## Slide 16: Minimum Mode Pin Specification
Hold Acknowledgment.
When acknowledged, it relinquish the bus to the requesting device
HOLD
To request for bus by another device.
It is an active HIGH signal.

## Slide 17: Minimum Mode Pin Specification
Active low write signal.
Writes data to memory or output device depending on signal.
Differentiates memory access from I/O access.
When high, memory is accessed.
When low, I/O devices are accessed.

## Slide 18: Minimum Mode Pin Specification
Data Enable signal.
Used to enable a transceiver connected to the P
Data Transmit/Receive signal.
indicates the direction of flow through the transceiver.
When high, data is transmitted out i.e. written to.
When low, data is received in i.e. read in.

## Slide 19: Minimum Mode Pin Specification
Address Latch Enable
indicates an address is available on bus
active high during state

## Slide 20: Minimum Mode Pin Specification
An active low signal.
An interrupt acknowledge signal.
When microprocessor receives an INTR signal, it acknowledges the interrupt by generating this signal
When low it indicates an interrupt is being serviced.

## Slide 21: Maximum Mode Pin Specification
Instruction queue status.
Instruction queue is 6 bytes long
 |  | Function
0 | 0 | No Operation. During the last clock cycle, nothing was taken from the queue.
0 | 1 | First Byte. The byte taken from the queue was the first byte of the instruction.
1 | 0 | Queue Empty. The queue has been reinitialized as a result of the execution of a transfer instruction.
1 | 1 | Fetch subsequent byteSubsequent Byte. The byte taken from the queue was a subsequent byte of the instruction.
 |  | Function
0 | 0 | No Operation. During the last clock cycle, nothing was taken from the queue.
0 | 1 | First Byte. The byte taken from the queue was the first byte of the instruction.
1 | 0 | Queue Empty. The queue has been reinitialized as a result of the execution of a transfer instruction.
1 | 1 | Fetch subsequent byteSubsequent Byte. The byte taken from the queue was a subsequent byte of the instruction.

## Slide 22: Maximum Mode Pin Specification
Status Signals.
indicate operation done by the microprocessor
Related to memory and I/O access control signals.
 |  |  | Function
0 | 0 | 0 | Interrupt acknowledgement
0 | 0 | 1 | Read data from I/O port
0 | 1 | 0 | Write data from I/O port
0 | 1 | 1 | Halt
1 | 0 | 0 | Opcode fetch
1 | 0 | 1 | Memory read
1 | 1 | 0 | Memory write
1 | 1 | 1 | Passive state
 |  |  | Function
0 | 0 | 0 | Interrupt acknowledgement
0 | 0 | 1 | Read data from I/O port
0 | 1 | 0 | Write data from I/O port
0 | 1 | 1 | Halt
1 | 0 | 0 | Opcode fetch
1 | 0 | 1 | Memory read
1 | 1 | 0 | Memory write
1 | 1 | 1 | Passive state

## Slide 23: Maximum Mode Pin Specification
When low, all interrupts are masked
Indicates to other processors to not request for system bus.
No HOLD request is granted.
No bus is relinquished to the other processors

## Slide 24: Maximum Mode Pin Specification
Request/Grant pins.
Other processors request the CPU through these for system bus.
CPU sends acknowledge signal on the same lines.
.

## Slide 25: QUIZ
Assuming you want to type a secret message using a keypad connected to an 8086 microprocessor, deduce the values of the following pins during that time. Justify your answers too.
    e.g. mention if low (0) / high (1) and why.
Do you think there may be other pins involved? If so, justify your answer.

## Slide 26: Thank You !!